## Slide 1
RESEARCH REPORT · 2026
Elevator Vertical Distance Estimation
Predicting how far an elevator travelled — using only the sensors in your pocket.
Eyal Yakir · Uriya Cohen-Eliya
Smartphone Inertial & Pressure Sensing
April 2026

## Slide 2
INTRODUCTION
The Problem
02
A phone in your pocket. An elevator ride. How far did you actually travel — vertically?
a
Detect the ride
Find when the elevator started and stopped — purely from the IMU.
b
Estimate Δh
Predict the signed vertical distance (up or down) in metres.
c
Quantify uncertainty
Return a calibrated 90 % confidence interval, not just a point estimate.

## Slide 3
INTRODUCTION
End-to-End Pipeline
03
Two stages, one shared idea: model the physics, then quantify the noise.
Sensor stream
Accelerometer + pressure (~50–100 Hz)
Segmentation
Slice ride intervals up / down / outside
Quality filter
Per-segment σ reject low-SNR
Prediction
Δh + 90 % CI 3 algorithms
Calibration
Split-conformal coverage guarantee
OUTPUT
Per-ride signed Δh in metres with calibrated [Δh – δ , Δh + δ] interval.

## Slide 4
INTRODUCTION
Data Collection
04
Multi-phone simultaneous recording across seven elevators in three cities.
7
Elevators
6
Buildings
3
Cities
4
Phones / ride
397
Labelled rides
Buildings
Millenium Hotel — Internal
Ra'anana
Millenium — Outside elevator
Ra'anana
Acro
Ra'anana
Beit Mansour
Ra'anana
Beit Yitzchaki
Ra'anana · held-out test
BarIlan-2
Herzliya
Haari
Ramat Gan
Protocol
All four phones recording in sync (one in each pocket).
Ride pattern: full traversal up, then descent.
Stationary windows before and after each ride for gravity calibration.
Barometer (where available) provides ground-truth altitude via ISA inversion.
Beit Yitzchaki withheld as test set — never seen during tuning.

## Slide 5
INTRODUCTION
Storyline
05
Where this hour will take us.
01
Physics
Jerk-limited S-curves and what an elevator looks like to an IMU.
02
Detection
Matched-filter pair detection on the accelerometer; F1, IoU.
03
Prediction
Three algorithms to predict Δh: barometer, ZUPT, trapezoid pulse-pair.
04
Uncertainty
Per-segment σ, quality filter, split-conformal calibration.
05
Results
Held-out: 89.4 % within ±1.5 m, MAE 1.49 m, median 0.30 m.
06
Product
Boutique pipeline — a Streamlit wizard producing a Hebrew PDF report.

## Slide 6
INTRODUCTION
Building Heights — Diversity of the Dataset
06
Total traversable height per elevator. Spans short residential to multi-storey hotel.
Fig. Sum of signed Δh across all rides per elevator.

## Slide 7
Act II · Physics
How elevators look to an inertial sensor

## Slide 8
PHYSICS
Elevator Kinematics — A Jerk-Limited S-Curve
07
What the IMU sees
Velocity v(t)
Smooth S-curve — no kink at peak.
Acceleration a(t)
Two trapezoid lobes — one positive, one negative.
Jerk j(t) = ä
Bounded; this is what makes the ride comfortable.
Gravity dominates
|a| ≪ g. Subtract gravity carefully or estimates blow up.

## Slide 9
PHYSICS
Seven Phases of an Ideal Ride
08
Fig. Velocity (top) and acceleration (bottom) versus time. The seven phases mirror the jerk profile.

## Slide 10
PHYSICS
The Trapezoid Template — What We Actually Fit
09
Why a trapezoid?
A perfect ride produces an acceleration profile composed of two trapezoid lobes: positive at start, negative at end. We replace the smooth S-curve with this idealised shape. Three free parameters per lobe:
a₀
plateau amplitude
τ_r
ramp duration
τ_p
plateau duration

## Slide 11
Act III · Detection
Finding ride intervals on the IMU

## Slide 12
DETECTION
Matched-Filter Detection
10
Cross-correlate the ideal pulse with the measured signal.
Sweep a single trapezoid template across the time series.
Output: response score r(t) — high where the shape matches.
Adaptive threshold τ on r(t) yields candidate ride starts/ends.
Coarse first pass over a grid of τ_r, τ_p, a₀ values.

## Slide 13
DETECTION
Pair Filter — Eliminating False Lobes
11
Each ride must have BOTH a positive and a negative lobe within a sensible time window.
Positive lobe
Acceleration phase — elevator speeds up
Plateau gap
Coasting at constant speed — skipped by the filter
Negative lobe
Deceleration phase — elevator slows down

## Slide 14
DETECTION
Detection Headline
12
Stable across the held-out building. IoU-aware metrics confirm tight ride bounds.
TRAIN · 5 buildings
0.813
F1* (best operating point)
0.642
IoU-F1 @ 0.5 — ride-bound quality
TEST · Beit Yitzchaki (held out)
0.875
F1*
0.830
IoU-F1 @ 0.5
F1* is the F1 at the optimal threshold; IoU-F1@0.5 requires ≥ 0.5 overlap with the GT interval.

## Slide 15
DETECTION
Failure Modes — Where Detection Slips
13
What goes wrong
Walking confusion
Steady gait amplitude can mimic an acceleration lobe.
Short rides
1–2 floor traversal: lobes overlap, no plateau.
Phone re-orientation
Pocket repositioning produces a transient impulse.
Building harmonics
Older shafts add 1–3 Hz oscillation atop the pulse.

## Slide 16
DETECTION
How Tight Are the Ride Bounds?
14
Distribution of IoU between detected and ground-truth ride intervals. Modes near 0.85 — bounds are tight.

## Slide 17
Act IV · Prediction
Three algorithms for vertical distance

## Slide 18
PREDICTION
Three Algorithms for Δh
15
Each leverages different physics. We use whichever the phone can support.
Barometric ISA
Pressure → ISA altitude inversion. Needs a barometer (≈ 60 % of phones). Cleanest signal — used as ground truth where available.
Δh = h_ISA(p₂) − h_ISA(p₁)
ZUPT integration
Subtract gravity, integrate twice. Zero-velocity-update at start/end pins drift. Works on every phone but accumulates noise.
Δh = ∬ aᵥ(t) dt² , with ZUPT
Trapezoid pulse-pair
Fit the seven-segment trapezoid template to the measured acceleration. Closed-form Δh from plateau parameters; robust to baseline drift.
Δh = a₀ τ_p (τ_r + τ_p)

## Slide 19
PREDICTION
ZUPT — Double Integration
16
Zero-Velocity Update
Step 1.
Subtract gravity using stationary pre/post windows.
Step 2.
Integrate vertical acceleration → velocity v(t).
Step 3.
Pin v(0) = v(T) = 0 — both endpoints are stationary.
Step 4.
Integrate v(t) → Δh.
Drift cancels at the endpoints; bias from any residual gravity error scales with T².

## Slide 20
PREDICTION
Trapezoid Pulse-Pair — Shared-Shape Fit
17
Why share parameters?
A real elevator uses the same jerk profile to accelerate and to decelerate. So both lobes share τ_r and a₀, with sign-flipped polarity. Joint least-squares over the pair halves the parameter count and doubles the effective SNR.
Δh = a₀ · τ_p · (τ_r + τ_p)

## Slide 21
PREDICTION
Joined Pulse — When Rides Are Too Short
18
Short-ride regime
On 1–2 floor rides the cabin reaches maximum speed only briefly — or never reaches it at all. The two lobes overlap. We collapse to a single joined-pulse model with no plateau:
Δh = ½ · a₀ · τ_r²
Detection switches between the two automatically based on plateau length τ_p.

## Slide 22
PREDICTION
Per-Segment σ and the Quality Filter
19
Not every ride is equally informative. We compute a closed-form noise estimate per segment and reject the worst.
Closed-form per-segment σ
σ_Δh² = σ_a² · ∂Δh/∂a₀ + σ_τr² · ∂Δh/∂τ_r + σ_τp² · ∂Δh/∂τ_p
Each ∂Δh/∂θᵢ from the trapezoid Jacobian.
Sensor noise σ_a estimated from the pre-stationary window.
Geometry noise σ_τ from CRB on the matched-filter response.
Quality rule
Drop any prediction whose σ_Δh exceeds 1.5 m — these are rides where the model itself says “I'm uncertain”.
≈ 8%
of rides flagged & dropped
≈ 25%
MAE reduction on the rest

## Slide 23
PREDICTION
Split-Conformal Calibration
20
Per-segment σ gives a Gaussian-tail interval — but the residuals aren't Gaussian. We re-calibrate.
1. Hold-out
Reserve 20 % of training rides as a calibration split.
2. Score residuals
On the calibration split, compute |Δh − Δĥ| / σ̂.
3. Pick quantile
Take the 90th-percentile of those scores → multiplier q.
Final interval
Δĥ ± q · σ̂ ⟹ marginal coverage ≥ 90 %.

## Slide 24
Act V · Results
Held-out performance

## Slide 25
RESULTS
Headline Numbers — Held-Out Test
21
Pooled across both prediction algorithms with matched-segmenter; n = 397 rides.
89.4 %
within ± 1.5 m
1.49 m
MAE
0.30 m
median |error|
By algorithm
Algorithm
median |error|
coverage @ 90 %
ZUPT
0.19 m
94.4 %
Trapezoid pulse-pair
0.29 m
93.5 %

## Slide 26
RESULTS
Predicted vs True Δh — Train
22
ZUPT (left) · Trapezoid pulse-pair (right). Closer to y = x is better.

## Slide 27
RESULTS
Error CDFs — Where Each Algorithm Lives
23
CDF of |Δh − Δĥ| on train (left) and test (right). Median error stays sub-half-metre on test.

## Slide 28
RESULTS
Per-Segment Confidence Intervals
24
Each ride: prediction ± 90 % CI plotted against true Δh. Bands widen on harder rides — exactly as designed.

## Slide 29
RESULTS
Coverage and MAE by Ride Length
25
Coverage holds at ≥ 90 % across short, medium, and tall rides. MAE scales sub-linearly with Δh.

## Slide 30
Act VI · Product
From research to a deliverable

## Slide 31
PRODUCT
Boutique Pipeline — End-to-End in 5 Steps
26
Streamlit wizard
1. Upload — drag & drop session zips.
2. Inspect — view raw signals + GT overlay.
3. Segment — edit detected ride bounds.
4. Predict — pick algorithm; see Δh + CI.
5. Report — generate Hebrew PDF deliverable.

## Slide 32
PRODUCT
Step 3 — Segmentation Review
27
Detected ride intervals are editable. The user accepts, splits, or deletes any candidate before prediction.

## Slide 33
PRODUCT
The Hebrew PDF Deliverable
28
What it contains
Per-elevator summary table
All rides with predicted Δh + CI
Quality flags for low-SNR rides
Ground-truth overlay where available
Hebrew RTL layout, A4 portrait

## Slide 34
Act VII · Closing

## Slide 35
CLOSING
What We Learned
29
Three takeaways from a year of riding elevators with phones in our pockets.
Physics first, ML second
A tight kinematic prior — the trapezoid template — beat black-box alternatives at every stage. Detection AND prediction.
σ is a feature, not an output
Letting the model report its own uncertainty unlocked the quality filter, the CI, and downstream calibration.
Cross-phone is the real test
Numbers from a single phone are misleading. Four-phone simultaneous recording was decisive in catching biases.

## Slide 36
Q & A
Thank you.
Eyal Yakir · Uriya Cohen-Eliya
30

## Slide 37
APPENDIX · HIDDEN
Detector Hyperparameter Walkthrough
31
Coarse grid → refine. Defaults chosen on the train fold; never re-tuned on test.
Parameter
Search range
Default
Source
τ_r ramp duration
0.5 – 1.5 s
0.9 s
Ride dynamics
τ_p plateau duration
0.0 – 6.0 s
1.5 s
Lobe length
a₀ plateau amplitude
0.4 – 1.4 m/s²
0.9 m/s²
Cabin spec
τ_thr detection threshold
2 – 6 σ
3 σ
Adaptive
Δt_pair pair gap window
0.5 – 30 s
auto
Per-ride bound

## Slide 38
APPENDIX · HIDDEN
Per-Experiment Detection Breakdown
32
Detection metrics by building. Beit Yitzchaki is the held-out test set.
Building
F1*
IoU-F1 @ 0.5
Millenium Hotel — Internal
0.84
0.69
Millenium — Outside
0.79
0.61
Acro
0.82
0.65
Beit Mansour
0.83
0.68
BarIlan-2 (Herzliya)
0.78
0.59
Haari (Ramat Gan)
0.81
0.64
Beit Yitzchaki (HOLD-OUT)
0.875
0.830

## Slide 39
APPENDIX · HIDDEN
Trapezoid σ — CRB Derivation
33
We derive a Cramer-Rao lower bound on σ_Δh given the trapezoid Jacobian and white sensor noise.
y(t) = T(t; θ) + ε(t), ε ~ N(0, σ_a² I)
I(θ) = (1/σ_a²) · J(θ)ᵀ J(θ) Fisher information
Cov(θ̂) ≥ I⁻¹(θ) Cramer-Rao
σ_Δh² = ∇_θ Δh ᵀ · I⁻¹(θ) · ∇_θ Δh delta-method
with ∇_θ Δh = ( τ_p(τ_r+τ_p), a₀ τ_p, a₀(τ_r + 2τ_p) )

## Slide 40
APPENDIX · HIDDEN
ZUPT — Noise Budget
34
Three error sources dominate ZUPT estimates. Each scales differently with ride duration T.
Sensor white noise
σ_h ∝ σ_a · T^{1.5} / √(N)
Reduced by sampling rate ↑ and stationary calibration.
Gravity bias
σ_h ∝ Δg · T²
Worst at long rides. Mitigated by per-ride gravity estimate.
Tilt error
σ_h ∝ sin(δθ) · g · T²
Mitigated by long stationary windows; pocket motion remains a risk.

## Slide 41
APPENDIX · HIDDEN
Ground-Truth Audit — Four-Phone Cross-Check
35
Each ride is recorded by four phones simultaneously. We use the cross-phone disagreement as a GT noise floor.
0.08 m
median cross-phone σ
99.2 %
rides agree within ±0.5 m
12 / 397
manual edits required
Where the barometer agrees with the trapezoid+ZUPT cross-check across all four phones, we trust the GT to ±10 cm. The handful of edits address PRS dropouts.

## Slide 42
APPENDIX · HIDDEN
Worst-Prediction Case Studies
36
Two failure cases. Left: short ride with overlapping lobes. Right: pocket reorient mid-ride.

## Slide 43
APPENDIX · HIDDEN
Architecture / File Layout
37
Two-stage pipeline; each stage is a Pydantic-configured dispatcher.
src/segmentation/
Stage 1 — Segmenter dispatcher; two algorithms (matched-filter, pressure-filter).
src/prediction/
Stage 2 — Predictor dispatcher; three algorithms (barometer, ZUPT, trapezoid).
src/utils/
Stage-agnostic helpers — gravity removal, conformal calibrator, pulse fits.
src/data/
Loaders, GT editor, dataset definitions.
src/pipelines/
End-to-end Streamlit Boutique Pipeline.
docs/latex/
This report; LaTeX source + figures.